## Slide 1: Computer Networks and the Internet: An Overview
Chapter 1

## Slide 2: Roadmap
Internet structure
  overview
  protocols
  core, edge, access
Packet vs circuit switching
Performance metrics
  loss, delay, throughput
Internet layers

## Slide 3: The Internet: "a network engineer" view
Internet
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network
Packet switches: forward packets (chunks of data)
  routers, switches
Communication links
  fiber, copper, radio, satellite
  transmission rate: bandwidth
Billions of connected computing devices:
  hosts = end systems
  running network apps at Internet’s “edge”
Networks
  collection of devices, routers, links: managed by an organization
Notes: View 1: The Internet behind the scenes: end devices, routing devices, links, protocols, etc.
Main players: AT&T, Verizon, Akamai, etc. Access providers.

## Slide 4: The Internet: "a network engineer" view
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network
Ethernet
HTTP
Skype
IP
WiFi
4G
TCP
Streaming
video
"network of networks"
protocols are everywhere:
  control sending, receiving of messages
  e.g., HTTP, Skype, TCP, IP, WiFi, 4G/5G, Ethernet
standards
  protocol ~ algorithm
  standard ~ template, objectives
  important standardization bodies: RFC, IETF, IEEE
Notes: Standards vs protocols:
Standards are broad descriptions/specifications of how systems should work. Think of standards as blueprints.
Protocols are a specific set of rules that govern the exchange of data between devices. Think of protocols as detailed instructions based on a blueprint.
A programming analogy: standards are to documentation what protocols are to algorithms.

## Slide 5: The Internet: "a software engineer" view
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network
HTTP
Skype
Streaming
video
Infrastructure that provides services to applications:
  web, streaming, email, games, social media…
Provides programming interface to distribute applications:
  "hooks" allowing apps to send/receive messages (e.g., socket programming)
  "service options," analogous to postal service (e.g., reliable vs unreliable data transfer)
Notes: View 2: The Internet as a platform to provide services.
Analogy: Think of an API. One can use the Internet through its "APIs" to provide services.
Main players: Netflix, Facebook/Meta, etc. Content providers.
This course is comprehensive and explores both views.

## Slide 6: What’s a protocol?
Human protocols:
“what’s the time?”
“I have a question”
introductions
Network protocols:
computers (devices) rather than humans
all communication activity in Internet governed by protocols
Protocols define the format, order of messages sent and received among network entities, and actions taken on message transmission, receipt
Rules for:
… specific messages sent
… specific actions taken when message received, or other events
Notes: Can you think of any other human protocols?
Can you think of any computing protocols?
Why do we need this many protocols, both for humans and computers?

## Slide 7: What’s a protocol?
A human protocol and a computer network protocol:
Hi
Hi
Got the
time?
2:00
time
TCP connection
response
<file>
TCP connection
request
GET http://gaia.cs.umass.edu/kurose_ross
Notes: Explain important points
distributed entities, exchanging messages (governed by protocols)
Time going down
go over definition of protocol (showing format, order of messages sent and received, and actions taken)
We’ll see these kinds of diagrams a lot

## Slide 8: Internet structure
network core:
  mesh of interconnected routers, networks
network edge:
  hosts: clients and servers
  servers often in data centers
access network:
  wired, wireless links
  often used to describe last-mile links (e.g., WiFi, 4G/5G, DSL)
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network
Definition: ISP (Internet Service Provider): entity/organization that manages a given network

## Slide 9: Internet structure
network core:
  mesh of interconnected routers, networks
network edge:
  hosts: clients and servers
  servers often in data centers
access network:
  wired, wireless links
  often used to describe last-mile links (e.g., WiFi, 4G/5G, DSL)
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network

## Slide 10: Internet structure
network core:
  mesh of interconnected routers, networks
network edge:
  hosts: clients and servers
  servers often in data centers
access network:
  wired, wireless links
  often used to describe last-mile links (e.g., WiFi, 4G/5G, DSL)
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network

## Slide 11: Data transfer: Two broad approaches
1- Circuit switching:
resources reserved for "call" between source and destination
pre-defined route to destination
guaranteed performance
data often transmitted in streams

## Slide 12: How to reserve resources?
Old telephone systems:
telephone operator physically interconnected source and destination
reserved, exclusive link between end devices
Telephone exchange

## Slide 13: How to reserve resources?
Modern approaches:
Frequency Division Multiplexing (FDM)
  optical, electromagnetic frequencies divided into narrow frequency bands
  each call/user allocated its own band
Time Division Multiplexing (TDM)
  time divided into slots
  each call/user allocated periodic slots
frequency
time
frequency
time
4 users

## Slide 14: Data transfer: Two broad approaches
2- Packet switching: store-and-forward
hosts break messages into packets
packets are stored and forwarded one at a time (e.g., first-in, first-out)
no resource reservation; no pre-defined route to destination
no performance guarantees
source
router
R bps
destination
1
2
3
L bits
per packet
R bps

## Slide 15: Circuit switching vs Packet switching
1 Gbps link
each user:
  needs 100 Mbps when "active"
  active 10% of time
Q: How many users can be served using circuit switching?
N
users
1 Gbps link
…..
A: 10 users

## Slide 16: Circuit switching vs Packet switching
1 Gbps link
each user:
  needs 100 Mbps when "active"
  active 10% of time
Q: How many users can be served using packet switching?
N
users
1 Gbps link
…..
A: with 35 users, probability > 10 active users at same time is less than 0.004.

## Slide 17: Is packet switching a winner?
The Internet uses packet switching.
Pros | Cons
great for bursty data (sometimes has data to send, sometimes does not) resource sharing simple (no "call" setup) | excessive congestions possible no performance guarantees

## Slide 18: Packet switching: Queueing
What if more than one user is active at a time? If arrival rate (in bps) to link exceeds transmission rate (bps) of link for some time:
packets will queue, waiting to be transmitted on output link
packets can be dropped (lost) if memory (buffer) in router fills up
A
B
C
R = 100 Mb/s
R = 1.5 Mb/s
D
E
queue of packets
waiting for transmission over output link

## Slide 19: How packet delay occurs?
delay =
transmission delay: rate information is transmitted to link
  L: packet size (bits)
  R: link transmission rate (bps)
propagation
nodal
processing
queueing
A
B
transmission

## Slide 20: How packet delay occurs?
delay =
propagation delay: travel time
  d: length of physical link
  s: propagation speed (~ m/s)
propagation
nodal
processing
queueing
A
B
transmission

## Slide 21: How packet delay occurs?
delay =
processing delay:
  time to process packet headers
  time to check if packet is not corrupted
  function of "CPU power"
propagation
nodal
processing
queueing
A
B
transmission

## Slide 22: Queueing delay
depends on in and out rates
harder to estimate exactly
Useful metric: traffic intensity
: average packet arrival rate (pkt/s)
L: packet length (bits)
R: link transmission rate (bps)
La/R << 1: avg. queueing delay small
La/R -> 1: avg. queueing delay high (Q: what happens to "excess" packets?)
La/R << 1
La/R -> 1

## Slide 23: "Real" Internet delays and routes
traceroute program:
sends 3 packets that will reach router i on path towards destination
router i will return packets to sender
sender measures time interval between transmission and reply
3 probes
3 probes
3 probes

## Slide 24: Real Internet delays and routes
1 cs-gw (128.119.240.254) 1 ms 1 ms 2 ms
2 border1-rt-fa5-1-0.gw.umass.edu (128.119.3.145) 1 ms 1 ms 2 ms
3 cht-vbns.gw.umass.edu (128.119.3.130) 6 ms 5 ms 5 ms
4 jn1-at1-0-0-19.wor.vbns.net (204.147.132.129) 16 ms 11 ms 13 ms
5 jn1-so7-0-0-0.wae.vbns.net (204.147.136.136) 21 ms 18 ms 18 ms
6 abilene-vbns.abilene.ucaid.edu (198.32.11.9) 22 ms 18 ms 22 ms
7 nycm-wash.abilene.ucaid.edu (198.32.8.46) 22 ms 22 ms 22 ms
8 62.40.103.253 (62.40.103.253) 104 ms 109 ms 106 ms
9 de2-1.de1.de.geant.net (62.40.96.129) 109 ms 102 ms 104 ms
10 de.fr1.fr.geant.net (62.40.96.50) 113 ms 121 ms 114 ms
11 renater-gw.fr1.fr.geant.net (62.40.103.54) 112 ms 114 ms 112 ms
12 nio-n2.cssi.renater.fr (193.51.206.13) 111 ms 114 ms 116 ms
13 nice.cssi.renater.fr (195.220.98.102) 123 ms 125 ms 124 ms
14 r3t2-nice.cssi.renater.fr (195.220.98.110) 126 ms 126 ms 124 ms
15 eurecom-valbonne.r3t2.ft.net (193.48.50.54) 135 ms 128 ms 133 ms
16 194.214.211.25 (194.214.211.25) 126 ms 128 ms 126 ms
17 * * *
18 * * *
19 fantasia.eurecom.fr (193.55.113.142) 132 ms 128 ms 136 ms
traceroute: gaia.cs.umass.edu to www.eurecom.fr
* Do some traceroutes from exotic countries at www.traceroute.org
* means no response (probe lost, router not replying)
3 delay measurements from
gaia.cs.umass.edu to cs-gw.cs.umass.edu
3 delay measurements
to border1-rt-fa5-1-0.gw.umass.edu
looks like delays decrease! Why?
trans-oceanic link

## Slide 25: Throughput
average rate (bits/time unit) at which bits are being sent from sender to receiver
analogy: water pipes
link capacity
Rs bits/sec
link capacity
Rc bits/sec
server sends bits
(fluid) into pipe
(i.e., pipe that can carry
fluid at rate Rs)

## Slide 26: Throughput
Rs < Rc What is average end-end throughput?
Rs bits/sec
Rc bits/sec
Rs > Rc What is average end-end throughput?
link on end-end path that constrains end-end throughput
bottleneck link
Rs bits/sec
Rc bits/sec

## Slide 27: Throughput: network scenario
10 connections (fairly) share backbone bottleneck link R bits/sec
Rs
Rs
Rs
Rc
Rc
Rc
R
per-connection end-end throughput: min(Rc,Rs,R/10)
in practice: Rc or Rs is often bottleneck

## Slide 28: Layered Internet protocol stack
application: supporting network applications
  HTTP, IMAP, SMTP, DNS
transport: process-process data transfer
  TCP, UDP
network: routing of datagrams from source to destination
  IP, routing protocols
link: data transfer between neighboring network elements
  Ethernet, 802.11 (WiFi), PPP
physical: bits “on the wire”
link
application
network
transport
physical
application
transport
network
link
physical

## Slide 29: Why layering?
Layering is a common approach to designing complex systems. The explicit, modular structure
allows identifying relationship of system's pieces
eases maintenance, updating system

## Slide 30: Encapsulation
message
segment
datagram
frame
Matryoshka dolls (stacking dolls)
Credit: https://dribbble.com/shots/7182188-Babushka-Boi
Notes: Thanks to Nikko Bovornkeeratiroj, Phuthipong <phuthipong@cs.umass.edu>, for the stacking dolls idea and slides

## Slide 31: Services, Layering and Encapsulation
source
transport-layer protocol encapsulates application-layer message, M, with transport layer-layer header Ht to create a transport-layer segment
  Ht used by transport layer protocol to implement its service
application
transport
network
link
physical
destination
application
transport
network
link
physical
Transport-layer protocol transfers M (e.g., reliably) from one process to another, using services of network layer
Ht
M
Application exchanges messages to implement some application service using services of transport layer
M

## Slide 32: Services, Layering and Encapsulation
source
Transport-layer protocol transfers M (e.g., reliably) from one process to another, using services of network layer
Ht
M
network-layer protocol encapsulates transport-layer segment [Ht | M] with network layer-layer header Hn to create a network-layer datagram
  Hn used by network layer protocol to implement its service
application
transport
network
link
physical
destination
M
application
transport
network
link
physical
M
Ht
Hn
Network-layer protocol transfers transport-layer segment [Ht | M] from one host to another, using link layer services

## Slide 33: Services, Layering and Encapsulation
source
Ht
M
link-layer protocol encapsulates network datagram [Hn| [Ht |M], with link-layer header Hl to create a link-layer frame
application
transport
network
link
physical
destination
M
application
transport
network
link
physical
M
Ht
Hn
Link-layer protocol transfers datagram [Hn| [Ht |M] from host to neighboring host, using network-layer services
M
Ht
Hn
Hl
M
Ht
Hn
Network-layer protocol transfers transport-layer segment [Ht | M] from one host to another, using link layer services